## Slide 1: Respiratory Protection Training

## Slide 2: What is a Respirator

## Slide 3: Why is a Respiratory Necessary
MCOME staff that have direct contact with decedents, human remains and bodily fluids have the possibility of exposure to hazards such as Aerosol Transmissible Disease (ATDs)or Chemicals.
Respirators are one method to help lower this risk by reducing the concentration of inhaled contaminates.

## Slide 4: Aerosol Transmissible Diseases (ATDs)
ATDs are diseases or pathogens that can be aerosolized from bodily fluids and require airborne or droplet precautions.
  Examples include: influenza, tuberculosis, COVID, meningitis, etc.
Autopsies, blood draws, and manipulating the decedent increase the risk of ATD exposure.

## Slide 5: Chemicals
Formaldehyde
  Colorless, strong smelling, and often found in aqueous solutions.
  Commonly used as a preservative in medical laboratories and mortuaries.
    Formaldehyde sampling is being conducted to ensure exposure is below OSHA permissible exposure limit (PEL).
  Monitoring in our laboratory has shown exposure of formaldehyde in lab work areas during an 8-hour period is below OSHA PEL and respiratory protection is not required.
Acetonitrile
  Monitoring has shown exposure during disposal of acetonitrile is below OSHA PEL and respiratory protection is not required.
Butyl Chloride
  Monitoring of Butyl Chloride, or 1-chlorobutane is below OSHA PEL and respiratory protection is not required.

## Slide 6: Hierarchy of Controls Used to Reduce Risk
Engineering Controls
Administrative Controls
PPR (respirators)
Respirators are the last line of defense.

## Slide 7: Engineering Controls
Examinations
  Negative pressure Examination Suite with 15 air exchanges every hour
  Negative pressure Special Procedure Suite with 30 air exchanges every hour
  Down draft tables
  Designed to pull the contaminants away from OME personnel

## Slide 8: Engineering Controls
Laboratory
  All fume hoods are inspected and certified annually
  All chemical storage areas are adequate and well ventilated
  General and local ventilation – including use of fume hoods
  Enclosure or confinement of a work process or operation
  Substitution of less toxic materials, where feasible, to reduce or eliminate respiratory hazards

## Slide 9: Administrative Controls
All Departments
  Ensure all department personnel have adequate training to conduct their duties safely.
    Bloodborne Pathogen Training and availability of appropriate PPE
    Hazardous Communication Training
  MCOME has a separate body storage cooler for the storage of decomposed or possibly hazardous cases.
  Restricted access to areas with potential exposure to ATDs and/or chemicals
  Caution stickers are placed on remains pouches when a potential hazard is present
  Continual evaluations of procedures looking for ways to reduce exposure

## Slide 10: Administrative Controls
All Departments(cont.)
  Surveillance will be maintained of changes in work area conditions or changes to the degree of employee exposure or stress that may affect respirator effectiveness.
Admitting
  Cases believed to be infectious or hazardous are released from the Special Procedures cooler
Examinations
  Cases believed to be infectious or hazardous are examined in the Special Procedures suite
  Embalmed bodies are examined in the Special Procedures Suite

## Slide 11: Administrative Controls
Investigations
  Responding only when the environment has been deemed safe
  Request for decontamination is made prior to response and transport when needed
Laboratory
  Posting of appropriate signs to identify hazards
  Requiring all procedures for chemical safety, including the laboratory chemical hygiene plan, to be observed at all times.

## Slide 12: Respirators
There are two types of respirators
  Air purifying - uses a filter, cartridge, or canister to remove contaminants from the air the wearer breathes.
    Particulate, elastomeric, and powered air purifying (PAPR)
  Atmosphere supplying - provides the wearer clean air from an uncontaminated source.
    Air supplied and self-contained breathing apparatus (SCBA)

## Slide 13: N95 Particulate Respirator
Air purifying respirator that filters 95% of airborne particles 0.3 microns or greater.
  Not intended to filter chemicals from the atmosphere.
Requires a tight-fitting seal to protect the wearer.
  Facial hair can interfere with this seal

## Slide 14: N95
MCOME requires employees to wear a N95 respirator when:
  At all death scenes
  In the examination suite while aerosolizing procedures are being performed and until cleaning is completed
  In the admitting department when releasing a decedent to a funeral home or other agency
  In the laboratory when there is a suspicion of aerosol production or residuals which may be harmful
Video

## Slide 15: N95
If the N95 respirator malfunctions or breaks while being used:
  Move to an uncontaminated area and remove the N95 with as little cross contamination as possible.
  Replace any cross contaminated PPE and don a new N95.
If you notice continuous issues with the N95 please report the issue to your supervisor.
  Supervisors should notify the safety committee

## Slide 16: N95 DONNING, DOFFING, AND SEAL CHECK
Video

## Slide 17: N95 Donning, Doffing, and Seal Check
Instructions for each make and model of N95 used at MCOME are posted in the following locations:
  PPE supply room attached to the aseptic OR
  In the supply room and the transport vehicles
  Histology
  Accessioning
  In the main laboratory near the SDS folder
  On the cabinet door in the releasing corridor
Additional copies can be found in the Share Documents folder on under the Safety tab in SharePoint

## Slide 18: N95 MAINTENANCE AND STORAGE
In most cases N95 respirators can be used for an entire shift and then discarded.
  N95 respirators may be reused as long as the structure and seal remain intact
  N95s should be changed when there is a malfunction, deformity, contamination of the respirator, or breathing becomes difficult.
Video
MCOME will provide paper bags for each employee to store used non-contaminated N95 respirators until the next use.
N95 respirators used during examinations should be discarded when staff leaves the Examination Suite.

## Slide 19: Powered Air Purifying Respirators (PAPR)
PAPRs use a motor to blow clean air to the wearer by pulling contaminated air through canisters or cartridges.
PAPRs are loose fitting and do not require a fit test.
Video

## Slide 20: PAPR
MCOME has 8 Sentinel XL CBRN PAPR units (3 for Investigations, 3 for Examination, and 2 for the Laboratory).
The use of PAPRs during an examination or at a death scene is required as outlined in the Respiratory Protection Protocol or as determined by the MCOME Safety Committee.
PAPRs will be used in the Laboratory when noxious chemicals are being used or there are chemical spills and the concentration is known to be below OSHA permissible exposure limit
Staff being asked to wear a PAPR will receive “Just in Time Training” by trained MCOME staff

## Slide 21: N95 MAINTENANCE AND STORAGE​
In most cases N95 respirators can be used for an entire shift and then discarded. ​
N95 respirators may be reused as long as the structure and seal remain intact​
N95s should be changed when there is a malfunction, deformity, contamination of the respirator, or breathing becomes difficult. ​
MCOME will provide paper bags for each employee to store used non-contaminated N95 respirators until the next use.
N95 respirators used during examinations should be discarded when staff leaves the Examination Suite.

## Slide 22: PAPR Donning and Doffing
Video

## Slide 23: PAPR Batteries
The batteries used at MCOME are a rechargeable NiMH.
When fully charged, the batteries have a run time of approximately 8 hours.
The batteries require approximately 5 hours to develop a full charge.
  The LED on the charging unit will flash green when fully charged.
An alarm will sound when only 30 minutes of battery power remain.

## Slide 24: PAPR Cartridges
The useful service life of chemical cartridges will depend upon multiple factors (flow rate, concentration of contaminants, environmental conditions)
Cartridges should be replaced when:
  The flow meter check fails
  Smell, taste or irritation from the contaminant is detected
  If cartridges become soiled, damaged or breathing resistance occurs
  After leaving a hazardous environment

## Slide 25: PAPR Cleaning
PAPRs should be cleaned with a 10% solution of bleach followed by a water wipe/rinse.
The hood should be cleaned by wiping vertically from the top of the hood to the bottom of the hood (bib).
When cleaning the butyl hose covering, do not make contact with the inner hose as bleach will degrade the inner tubing.
Wipe all parts of the belt and blower unit.
While cleaning, inspect all parts for signs of tears or malfunctions.

## Slide 26: PAPR Storage
Once dry, the hood and breathing tube should be folded flat and placed in the duffle bag.
Cartridges that have been used in a hazardous environment should be discarded.
  The Safety Committee will evaluate hazardous environments and provide discard recommendations.
Cartridges used in a non-hazardous environment can be sealed and reused if they pass an air flow check.
Batteries and blower units

## Slide 27: Medical Conditions and Respirator Use
Breathing through a respirator is more difficult than breathing in open air. People with lung diseases such as asthma or emphysema, elderly people, and others may have trouble breathing. People with claustrophobia may not be able to wear a full face piece or hooded respirator. People with vision problems may have trouble seeing while wearing a mask or hood. Employees must be medically evaluated before assigned to use a respirator.
If you experience difficulty breathing, shortness of breath, or vision problems while wearing a respirator: notify your nearest coworker, remove the respirator in a non-contaminated area, and notify your supervisor.

## Slide 28: Fit Testing
According to OSHA 1910.134(f) fit testing is required.
  Before initial use, when respirators change, and annually.
Fit testing must be completed with the same make, model, style, and size of respirator that will be used.
Additional testing will be conducted if there are changes in an employee’s physical condition that affect the respirator fit.
  Facial scaring, cosmetic surgery, changes in body weight

## Slide 29: Fit Testing cont.
1910.134 (g)(1)(A) – employer shall not permit respirators with tight-fitting facepieces to be worn by employees who have facial hair that comes between the sealing surface of the facepiece and the face or that interferes with the valve function.
MCOME performs a qualitative fit test using Bitrex solution or Saccharin solution

## Slide 30: Conclusion
All respirators require training in order to be properly used. If you do not use a respirator correctly, it is very likely that it will not adequately protect you and may even hurt you.
If you have any questions regarding the use of respirators or any part of this training, please contact one of the supervisors.

## Slide 32: Thank You